## Slide 1: Jacinto™ Automotive Processor
Jacinto 7 Ethernet Switch

## Slide 2: Agenda
Ethernet Switch IP Features Overview
Deep Dive – Software Architecture
  CPSW LLD
  Ethernet Firmware
EthFw Demos
Jacinto 7 EVM – CPSW support
Deep Dive – EthFw
  Folder Structure
  Docs organization
  Sample Examples
  CPSW and PHY integration
  Switch configuration & Debugging

## Slide 3: Ethernet SwitcH
IP Overview

## Slide 4: Ethernet Switch – CPSW Functional Block Diagram
Host Port – Classify and Routing to compute cores
External MAC / Ethernet Ports

## Slide 5: Ethernet Switch – Feature Overview
Top Level Features
9 Ports – 8 MAC Ports, 1 Host Port
Support for RMII, RGMII, SGMII, QSGMII
Packet Classification (64 classifiers) & filtering using L2/VLAN/L3
  InterVLAN routing support
  UDP/TCP Checksum offload
Multicast/broadcast rate limiter
  Reset isolation
Port Mirroring, Port Trunking
Switch
CPU
Port1
Port2
Port3
Port4
Port5
Port6
Port7
Port8
P1 FIFO
1/2.5G MAC1
SGMII
QSGMII
P2 FIFO
1G MAC2
P3 FIFO
1G MAC3
P4 FIFO
1G MAC4
SERDES
Lane1
4-port Group1
P5 FIFO
1/2.5G MAC5
QSGMII
P6 FIFO
1G MAC6
P7 FIFO
1G MAC7
P8 FIFO
1G MAC8
SERDES
Lane2
4-port Group2
Sharing w/ other SERDES / pins
SGMII/ RGMII/RMII
SGMII/ RGMII/RMII
SGMII/ RGMII/RMII
SGMII/ RGMII/RMII
SGMII/ RGMII/RMII
SGMII/ RGMII/RMII
Sharing w/ other SERDES / pins
SGMII
RGMII/RMII (pinmux)
RGMII/RMII (pinmux)
CPSW (Ethernet Switch) IP

## Slide 6: Ethernet Switch – Auto Use-cases entitlement
  Security
  L2/L3 address whitelisting, L2 address blacklisting
  Advanced classification and Policing based on L2/L3 headers using Port number, Priority, ONU, DA, SA, VLAN inner/outer, EtherType, IPSA and IPDA
  Policing for rate limiting matched flows – three color marking on policed rates with drop controls
Deep packet inspection via integrated compute cores
  AVB/TSN Features
IEEE802.1Qav – Egress AVB rate shaping
IEEE802.1Qbb and IEEE802.3x Flow control
TSN Features
      IEEE802.1Qbv/1Qaz time base scheduling
      IEEE802.3br/IEEE802.1Qbu Frame Preemption
  Safety Features
SECDED ECC protection of table entries
Ram error detection and correction (ECC) with full end to end packet protection (CRC)

## Slide 7: Ethernet Switch – Feature Summary
Forwarding Between Ports
VLAN-aware line rate L2 switching
Per-flow ingress port rate limiting, filtering
Per-port broadcast, multicast rate limit
Key Building Blocks
ALE with 1k entries
Classifier module for L2/L3 header inspection (96 HW classifier rules)
  Ingress port: Rate-limit, filter
  FlowID assignment for Host traffic
AVB, TSN features support
  Traffic shaper
L2/L3 HW Checksum offload
Inter-VLAN routing in HW
Traffic to Host DMA port
Classifier for header inspection
FlowID for packet steering and multiple queue support
Transmit from Host
Classifier support for rate-limit per flow
TSN support: Time aware scheduling, pre-emption, Traffic Shaping with 8 HW Priority queue/port
Per-port priority regeneration support
Firewall, Filter
L2-based filter (OUI deny, MAC authentication)
Classifier based L2/L3 filtering
  No match drop
  MAC multicast range, IP CIDR mask filtering
HW filter for untagged, IPV4, dual tag, IP fragment, L3 Next Header check
Traffic to Host Inter-VLAN routing
ALE match: traffic match to host port
Classifier: Flow matching for HW offload
HW offload for matched flow : packet header modification in HW
Classifier
Flow ID
DMA Logic
Ethernet Switch Subsystem
ALE
Traffic Shaper

## Slide 8: Ethernet SWITCH
Deep Dive –Software Architecture

## Slide 9: Ethernet Switch – Data Flow
CPSWx (Switch HW)
ETHFW (R5F)
Linux
(A72-x)
TI-RTOS
(MCU-x R5F-x)
AutoSAR
(MCU0 R5F-x)
Multiple CPUs on the SoC can perform network IO simultaneously using the switch once the switch is configured via the FW
Subsequent packet IO can happen directly between the CPU specific network stack and switch HW via UDMA
Switch configuration
Data/Packet IO
Config
Ethernet Firmware Supporting Multiple Clients

## Slide 10: Ethernet Switch – Data Flow Detailed
Direct Control Path
IPC Control Path
Direct Data Path
MAC Ports
Host Port
Configures Registers
(open ALE, MAC ports, MDIO, Stats, etc)
A72
(Remote Core)
Apps
Network Stack
CPSW Driver
OS
Attach Core
Attach Core
Alloc Resources
Alloc Resources
Rx Ch
Tx Ch
DMA Resources
Alloc Resources:
Rx Flow Num
Tx Ch Num
MAC Address
Submit and retrieve packet calls
Switch R5
(Master Core)
RM
Apps
Network Stack
CPSW Driver
MCU R5
(Remote Core)
OS
Apps
Network Stack
CPSW Driver
CPSW 9G
Submit and retrieve packet calls
A72 Virtual Net Dev (SDK1.0)
EthFw
AUTOSAR CPSW CDD (POST SDK1.0)

## Slide 11: Ethernet Switch – Ref. AUTO Use-case
MCU R5
A72
iproute2
brctl
ethtool
vconfig
tc
mstpd
lldpd
snmpd
lacp
mvrp
Bonds
Bridges
VXLAN
User
Kernel
RT Netlink
ethtool ioctl
switchdev driver
swp0
swp1
swp7
cpsw driver
swp1
CPSW_9G
CPSW_2G
MCU Domain
Main Domain
CPSW 2G Register
CPSW 9G Register
C7x/Other R5
OS
Apps
NDK
EMAC_LLD
Direct Control Path
IPC Control Path
Direct Data Path
HTTP
PDUR
Ethernet Interface
Ethernet Driver 2G
Ethernet Transceiver
Ethernet Switch Driver
Ethernet State Machine
TCP/IP
IPv4,ARP,ICMPv4
IPv6,NDP,ICMPv6
UDP,TCP,DHCPv4,DHCPv6
AVTP
PTP
BMCA
COMM
SOAD
CDD
CDD
TLS
SD
DNS
UDPNM
DoIP
ETHXCP
MIRROR
BSWM
RTE
COM
CDD
Customer Function
XML,JSON
SOME/IP
Application
Ethernet Driver 9G
Remote Configuration Client
Remote Configuration Client
Remote Configuration Client
EAPOL
Remote Configuration Server
Firmware Application API
TI-RTOS
IP Router
NDK
CPSW_LLD
Other Drivers
Main R5 (switch)
ALE
LLD
ENETPHY
LLD
802.1AS
AVB
SRP
NM
Apps
Ethernet Firmware (AUTO)
Demo app (AUTO)
Kernel driver (LCPD)
PDK CPSW LLD (AUTO)
Switch resident protocols

## Slide 12: Ethernet Switch – Software Stack
EthFw Software Stack
EthFw Submodules
CPSW LLD – driver layer for CPSW9G IP
CPSW Remote Configuration Server
  CPSW Remote Configuration RTOS Client
Switch Resource Manager
Switch Resident Protocols
  TCP/IP NDK
Switch Configuration App

## Slide 13: Ethernet SWITCH
Software Releases

## Slide 14: Ethernet Switch – EthFw 1.0: IS / IS NOT
Basic Switching
VLAN
RGMII
1G/100M
Host Port Packet Tx/Rx
Switch R5 as packet source/sink
IPC based switch configuration from other cores
Linux virtual netdev driver integration
  A72 data path
TCP/IP stack (NDK)
Multicast switching
InterVLAN routing
Network Security
Classifier/Policer
QoS/Packet Priority regeneration
Traffic Shaping
OS | CPSW 2G (Direct driver) | CPSW 9G (Virtual driver)
TI RTOS | Y | SDK 1.0
Linux | Y | SDK 1.0
AUTOSAR | Y | Post SDK 1.0
QNX | SDK 1.0 | Post SDK 1.0
Timesync (802.1ASrev)
Time aware scheduling (802.1Qbv) - EST
SGMII
RMII
QSGMII and 2.5 Gbps support
Port Mirroring
Port Trunking
IET (Interspersing express traffic)
ENET PHY – power mgt
Switch compliance testing
Time sensitive networking
SDK 1.0
Post SDK 1.0

## Slide 15: Ethernet SWITCH
Jacinto 7 EVM: CPSW Support

## Slide 16: Ethernet Switch – Jacinto 7 EVM Baseboard
MCU_ENET
  DP83867 RGMII PHY
  1 Gbps
  CPSW 2G MDIO bus
ENET_EXP DB
  1 x QSGMII Expansion Daughter Board
  Not supported as SDK1.0
ENET EXP BOARD
(QSGMII)
MCU_ENET
(RGMII)
With SDK1.0 only CPSW2G supported on Baseboard, GESI DB is needed for CPSW9G

## Slide 17: Ethernet Switch – GESI Board
1 x RMII PHY (Post SDK1.0)
  DP83822
  100 Mbps
  CPSW 9G MDIO bus
4 x RGMII PHYs
  DP83867
  1 Gbps
  CPSW 9G MDIO bus
RMII PORT 5

## Slide 18: Ethernet SWITCH
Demos

## Slide 19: Ethernet Switch – Firewall
CPSW_LLD
TI-RTOS
Main Domain R5
Config I/F
Data I/F
Switch Config
Utility
NDK
Forward
I/F
Filter Rules
Traffic Classification
Firewall
Demo Apps
J7 EVM
Linux PC
Linux PC
Packet Generator
Demo Packet Streams
Packet Capture
Packet verifier
Application
Demonstrate
  Packet classification Network security, firewall
    Filter on L2 header: OUI, SA, VLAN
    Filter on L3 header: frag, SA/DA
Differentiation
  Network security based on L2/L3 header fields (wire rate)
Timeline: SDK 1.0

## Slide 20: Ethernet Switch – Classification and InterVLAN Routing
CPSW_LLD
TI-RTOS
Main Domain R5
Config I/F
Data I/F
Switch Config
Utility
NDK
Forward
I/F
HW-routing
InterVLAN
Traffic Classification
Classification and Forwarding
Demo Apps
J7 EVM
Linux PC
Linux PC
Packet Generator
Demo Packet Streams
Packet Capture
Packet verifier
Application
Demonstrate
  Packet classification
    L2 header: addr, EtherType, VLAN, priority, port number
    L3 header: SA/DA
  InterVLAN routing
    Wire rate, up-to 4 routes
Differentiation
  Ethernet sharing across multiple cores / VMs
  HW packet header inspection/classification
  InterVLAN routing in HW at line rate
Timeline: SDK 1.1
VM1
(A72)
Packet Capture
Packet verifier
Application
SW Routing

## Slide 21: Gateway Demo: CAN  Ethernet
Code Composer Studio
PCAN PC Tool
Used to Load and Run Application on DRA80xM
Send & Receive MESSAGE - CAN & DRA82xM
UART console
For console O/P
Network Apps
Receive & Send MESSAGE -Ethernet & DRA82xM
MCU0 R5
Main Domain
R5
CAN Driver
M3 DMSC
SYSB
I
OS
Network Driver
CPSW9G
DMSC Firmware
Demo Routing Application
CSL FL/RL
MCUSS
NDK
PCAN Module
Ethernet Cable
Cable for CAN
RJ45
USB
DB9
RJ45
DRA82x EVM
PC/Laptop
JTAG
USB/UART
Demonstrates Latency and CPU Load for routing application
Shows early CAN response
AUTOSAR MCAL driver
RTOS driver for CAN + Linux for ETH:
CAN Driver
CSL FL/RL
SYSB
I
OS
Early CAN response
Routing SW using just R5F – Cortex A free for other application usage
<100us driver routing latency

## Slide 22: Ethernet SWITCH
Deep Dive – Ethernet Firmware

## Slide 23: Ethernet Switch – CPSW Integration
Integration into app:
  CPSW configuration parameters: ALE, MAC, Host, MDIO
  DMA configuration parameters
  Print/tracing functions
  CPSW init and open
  Resource Manager attach
  IOCTLs and helper functions
  MAC/PHY configuration
  Close sequence
NDK integration C-file template
CPSW LLD examples: loopback, sanity, NIMU

## Slide 24: Ethernet Switch – PHY Integration
PHY abstraction layer as part of CPSW LLD
  State machine based
  PHY-specific drivers can implement their own callbacks or reuse generic implementation
Runtime device to driver mapping based on PHY ID
Auto-negotiation and manual mode
Clause-22 support
“PHY Integration Guide” document provided as part of CPSW docs

## Slide 25: Ethernet SWITCH
Switch Configuration and Debugging

## Slide 26: Ethernet Switch – Switch Configuration
Default configuration loaded during EthFw init – part of
Run-time switch configuration supported Switch Config via Network (config GUI) & UART
Fig – UART Based Config
Fig – Switch Config GUI

## Slide 27: Ethernet Switch – Debugging
Debugging Infrastructure
  GEL Scripts
    HW error stats report.
    Dump Switch forwarding table
    PHY reg read/write configuration
  Debug and diagnostic APIs/IOCTLs
    DMA statistics
    Switch config dump IOCTLs
  Runtime configurable trace support
  GUI support to run stress tests, get switch statistics.
Fig – UART Based Config
Fig – Stress Test Connection

## Slide 28: Q & A

## Slide 29: backup

## Slide 30: Ethernet Switch – Key Usecases
J7
ARM R5F
Host port
  L2 Switching Usecase
  Traffic from any external port to any external port
J7
ARM R5F
Host port
  L2 Aggregator Usecase
  Traffic from multiple external ports aggregated and sent over external port
J7
ARM R5F
Host port
  L2 Switching with Traffic to/from
  Compute Cores
  Traffic from any external port to Jacinto 7 compute cores
A72
J7
ARM R5F
Host port
  PCIe / Ethernet Bridge
A72
PCIe

## Slide 31: Ethernet Switch – Integrated Switch Key Value Propositions
Use-case | Key Features | Software Enablement
Gateway – Network Security | IP address whitelisting Protocol whitelisting Rate limiting Traffic shaping MAC Authentication | ALE driver with full IP entitlement Support for switch configuration via AUTOSAR/Linux
IO Hub | Support for 2-port driver & 9-port driver to connect vehicle network to switch | Support for multicore data planes using packet based classifications (flows) Single driver supporting all CPSW IP variants on Jacinto 7, Maxwell, Pascal. Scatter-gather
Central Gateway | Programmable L3 routing InterVLAN routing (4 hardware routes) 200ms Ethernet response | AUTOSAR MCAL switch dev LCPD Virtual netdev driver TCP/IP stack (NDK integration) Performance optimizations
Ethernet Surround View | IET/EST 802.1AS (PTP) IEEE 802.1Qav (Forwarding) | Time sync support TSN support

## Slide 32: Ethernet Switch – Release Plan
Milestone | CPSW_LLD | EthFw | Demos | Date
SDK 0.8 | Basic Switching VLAN RGMII 1G / 100M Host TX / RX | Switch config via UART |  | 30 March 2019
SDK 0.9 Bring-up | Multicast switching InterVLAN routing Ethernet PHY | TCP/IP stack (NDK integration) Switch config via telnet A72 remote core support Main R5_1 as packet source/sink Bring-up complete on EVM | CAN ↔ Ethernet gateway L2 Switching – multicast, VLAN | 30 June 2019
SDK 1.0 RTM | Network Security Classifier/Policer QoS/Packet Priority regeneration Traffic Shaping | Linux A72 Virtual driver integration | Firewall Demo InterVLAN routing and Traffic Classification demo | 30 Sep 2019

## Slide 33: Ethernet Switch – Usecases Entitlement
Latency improvement to meet requirements
  Direct data path from AUTOSAR R5 to Switch – eliminates need of IPC
  Plan for TSN features to enable deterministic latency like EST, IET and switch FIFO tuning
Optimized ETH driver for CPU load
  Receive and transmit interrupt pacing
  Support for scatter-gather to enable zero copy transmit
  L3 checksum offload support
  Support for enabling InterVLAN routing in hardware
L3 routing
  Dedicated switch R5 for Ethernet switch (CPSW9G) control – can be controlled via AUTOSAR or Linux
  Multi-core support – support direct data path for each core (no IPC during data movement)
    Support for enabling hardware features to classify and route traffic to intended core
  Linux Virtual netdev driver & AUTOSAR Ethernet switch (CPSW9G) driver enablement

## Slide 34: Ethernet Switch – Customer Enablement & Demos
J7
Main R5F
Host port
J7
Main R5F
Host port
MCU R5F
A72
Linux Virtual MAC
L2 Switch Usecase
Traffic from any external port to any external port
Features:
  Switch config via UART
  VLAN
  Multicast
  RGMII, 100M / 1G
L2 Aggregator Usecase
Traffic from multiple external ports aggregated and sent over external port
Features:
  Network security
  Policer
  QoS / Packet priority regeneration
  InterVLAN routing
L2 Switching
with internal cores
Traffic from multiple external ports aggregated to J7 compute cores
Features:
  Traffic shaping
  Traffic classification
  TCP/IP (NDK) stack on Switch R5F
  Packet TX/RX from MCU R5F

## Slide 35: Ethernet SWITCH
Performance

## Slide 36: Ethernet Switch – Performance
Content to be added

## Slide 37: Ethernet Switch – Performance Measurment
Content to be added – CPU load, Network throughput

## Slide 38: Ethernet SWITCH
Switch Certification

## Slide 39: Ethernet Switch – Standards Ecosystem
IEEE 802.1/IEEE 802.3/IEEE 802.1Q
Basic Ethernet
IEEE 802.3az
Energy Efficient
IEEE 802.1AS/IEEE 802.1Qav/IEEE 802.1Qat
IEEE 1722/IEEE 1733
AVB
IEEE 802.1AS-Rev/IEEE 802.1Qbu/IEEE 802.1Qbv/802.1Qcc/802.1Qci/
802.1Qch/ 802.1CB/ 802.1CM
TSN
Standards Body
TC11
TSN switch
Avnu Profile
EthernetDriver
EthernetSwitchDriver
Special Interest Groups
Independent Test &
Certification Houses
Tier 1
TC11
OEM
TC8
Automotive
Security Penetration
Testing
Silicon Vendor

## Slide 40: Ethernet Switch – Roadmap
J7ES RTL 1.0
4Q 2018
Cadence test suite
for Switch DV
J7ES Samples
1Q 2019
Internal Pre-Certification
Test
IXIA Equipment
Cost : $0 (Plan on using ICSS team’s chassis.)
ESCRYPT test plan
Cost : $0 (available from SVA team)
AVNU test plan
Cost : $0 (available to TI as Avnu member)
AVNU pre-certification tools
Cost : $20,000 per annum for UNHIoL membership
(Share with ICSS team)
OPEN ALLIANCE TC 11 test plan
Cost : $0 (open access)
SDK 1.0
3Q 2019
Ruetz Systems
Switch Qualification Certification
Cost : unknown
UNHIoL
AVNU TSN switch certification
Cost : ~ $10K
ESCRYPT
Security pen test certification
Cost : ~ $50K
Timeline
TBD

## Slide 41: Ethernet Switch – Linux Virtual Net Driver