## Slide 1: Multi-core Time synchronization

## Slide 2: Agenda
Why Multi-core time synchronization?
Multi-core Ethernet architecture
Multi-core Time-synchronization design
  Time Sync Router Configuration
  Coupling remote core timer with CPTS
  Multi – core Time Synchronization sequence
Example

## Slide 3: Why Multi-core time synchronization?
In Multi-core Ethernet architecture of Jacinto 7 family of devices, the control path of CPSW9G IP is solely controlled by the Main domain R5 core(EthFw), preventing other cores in the SoC to change CPSW9G configurations.
Common Platform Time Sync (CPTS), one of the IP sub-module of CPSW9G used for packet time-stamping is also controlled solely by the EthFw.
EthFw uses this CPTS timer and synchronizes itself with a master in the network using PTP stack.
So, a mechanism to provide time synchronization support to time-sensitive applications on remote cores is necessary in Ethernet firmware.

## Slide 4: Multi-core Ethernet architecture
Direct Control Path
IPC Control Path
Direct Data Path
MAC Ports
Host Port
Configures Registers
(open ALE, MAC ports, MDIO, Stats, etc.)
A72
(Remote Core)
Apps
Network Stack
CPSW Driver
OS
Attach Core
Attach Core
Allocate Resources
Allocate Resources
Rx Ch
Tx Ch
DMA Resources
Allocate Resources:
Rx Flow Num
Tx Ch Num
MAC Address
Packet submit /retrieve calls
Switch R5
(Master Core)
RM
Apps
Network Stack
CPSW Driver
MCU R5
(Remote Core)
OS
Apps
Network Stack
CPSW Driver
CPSW 9G
Packet submit /retrieve calls
A72 Virtual Net Dev
EthFw
AUTOSAR CPSW CDD
Once the switch is configured via the firmware on Main R5, other CPUs on the SoC can perform network IO simultaneously without involving the Main R5 core.
Subsequent packet IO can happen directly between the CPU specific network stack and switch HW via UDMA.

## Slide 5: Multi-core Time-synchronization design
CPSW_9G
CPSW 9G Register
EAPOL
Remote Configuration Server
Firmware Application API
TI-RTOS
IP Router
NDK
CPSW_LLD
Other Drivers
Main R5 (EthFw)
ALE
LLD
ENETPHY
LLD
Apps
CPTS
LLD
Master clock
Time Sync
Ethernet firmware running on Main R5 core configures Time Sync PTP stack and enables it.
Time Sync PTP stack synchronizes CPSW’s CPTS timer with the Master clock in network.
Using Ethernet remote configuration framework, EthFw provides timer coupling support to remote cores, and let them subscribe for callback notifications.
Ethfw uses Time Sync Router to route remote core timer’s event to hardware push of CPTS timer.
CPTS timer timestamps every hardware push event from remote core and returns the timestamps.

## Slide 6: Time Sync Router Configuration
Time-sensitive
Application
CPTS Timer
Remote core’s Timer
Coupling is done periodically
TSR
CPTS
Remote
core
Hw Push
64-bit Time Stamp
GTC0/ TIMER[14-19]
GTC0
TIMER[14-19]
PWM
Remote Core
Coupling between remote core’s timer and CPTS timer is done through Hardware push events of CPTS and Time Sync Router(TSR).
With this a linear relation is established between CPTS & remote timer.
Once the relation is established, remote core can independently use this coupled timer locally.

## Slide 7: Coupling remote core timer with CPTS
iproute2
brctl
ethtool
vconfig
tc
mstpd
lldpd
snmpd
lacp
mvrp
Bonds
Bridges
VXLAN
RT Netlink
ethtool ioctl
switchdev driver
swp0
swp1
swp7
cpsw driver
swp1
Remote Configuration Client
Remote Configuration Client
CPSW_9G
CPSW 9G Register
EAPOL
Remote Configuration Server
Firmware Application API
TI-RTOS
IP Router
NDK
CPSW_LLD
Other Drivers
Main R5 (switch)
ALE
LLD
ENETPHY
LLD
Apps
CPTS
LLD
Grand Master
Time Sync
Time Sync SW
Register remote core’s timer with the CPTS timer
Direct Control Path
IPC Control Path
Direct Data Path
Ethernet Firmware (AUTO)
Demo app
Kernel driverr
PDK CPSW LLD (AUTO)
Switch resident protocols
Time Sync library provides get Time and Lookup event APIs to remote cores via existing rpmsg layer in EthFw.
In addition to this, remote core can use its local synchronized timer for getting current time.
Remote core

## Slide 8: Multi – core Time Synchronization sequence
Remote core
EthFw(with TimeSync)
Sets up DM TIMER[14-19] / GTC0 and enable periodic PWM output/ HW push output
Register HW Push
4. Allocates a Hardware Push Instance.
  Configures TSR to map the DM Timer’s PWM to the HW Push Instance
  Save the callback for the Hardware Push Instance
R5 runs PTP and synchronizes with the external master clock
When hardware push event occurs, remote core’s registered callback is called with CPTS timer value.
Call back with Event Info
Hw Push Time stamp value N
Hw Push Time stamp value N+1
With two consecutive Hw push Time stamp values, the DMTIMER/GTC to CPTS clock rate ratio and linear relationship are established.
IPC
Call CpswProxy_registerRemoteTimer with timer Information & call back function.
Call back with Event Info
Next Hw Push event
– Synchronized Time (CPTS time)
– Rate ratio
– Local Timer Value
– Constant value
.
.
.

## Slide 9: Example
EthFw RTOS Server(MCU2_0) and EthFw RTOS Client (MCU2_1) demonstrates Multi-core time synchronization.
EthFw RTOS Server enables Time Sync PTP stack on MAC port 2 in slave mode and synchronizes with available master clock in the network.
EthFw RTOS Client registers GTC timer used by it for coupling using TSR.
Using registered hardware push callback, client establishes a linear relation and stores it locally.
Whenever Client calls CpswRemoteApp_getSynchronizedTime(), the API computes synchronized time using current GTC time and the established linear relationship with CPTS timer.
– Synchronized Time
– Rate ratio
– GTC Timer Value
– Constant value

## Slide 10
© Copyright 2020 Texas Instruments Incorporated. All rights reserved.
This material is provided strictly “as-is,” for informational purposes only, and without any warranty.
Use of this material is subject to TI’s Terms of Use, viewable at TI.com